## Slide 1: Determining the Camera Response Function Short Presentation
Dominik Neumann
Chair of Pattern Recognition (Computer Science 5)
Friedrich-Alexander-University Erlangen-Nuremberg
2010-05-12

## Slide 2: The Camera Response
Scene
Radiance
Image
Irradiance
(RAW image)
Image
Intensity
(pixel values)
Camera
Processor
Sensor
- White Balancing
- Gamma Correction
- "Beautification"
   Camera
Response
Function
Notes: In practice: mapping of irradiance to intensity (CRF) is a collective effect of various camera internal operations and noise.

## Slide 3: Motivation
Various Computer Vision Algorithms require Image Irradiance
  Color Constancy
  Shape from Shading
  Inverse Rendering
  Creating accurate
  HDR-Images
But: Output of a usual camera is not linear
My task: Examination of methods for CRF Estimation
  “Using Geometry Invariants for Camera Response Function Estimation” (Ng et al.)
  “Radiometric Calibration from a Single Image” (Lin et al.)
Color Constancy: Images by Eva Eibenberger
Notes: When running algorithms on arbitrary|natural|real-world images (flickr, …) …
Accept additional error OR find methods for estimating CRF so that you can „remove“ the changes of the CR

## Slide 4: Camera Response Functions
Agfachrome CTPrecisa100 Green
Agfachrome RSX2 050 Blue
Agfacolor Futura 100 Green
Agfacolor HDC 100 plus Green
Agfacolor Ultra 050 plus Green
Agfapan APX 025
Agfa Scala 200x
Fuji F125 Green
Fuji F400 Green
Kodak Ektachrome-100plus Green
Kodak Ektachrome-64 Green
Kodak KAI0372 CCD
Kodak Max Zoom 800 Green
Irradiance
Intensity
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1
Sample CRFs from DoRF (Database of Response Functions)
(compiled by Grossberg and Nayar)
Notes: CRF are usually non-linear, monotonically increasing

## Slide 5: CRF Estimation: Geometry Invariants
Physics-based approch
   Separation of camera nonlinearities from reflectance-induced nonlinearities
Strategy
  Find set of "Locally Planar Irradiance Points" (LPIP)
     no more reflectance-induced nonlinearities
  Estimate CRF from this data
Main Steps of the Algorithm:
Compute Image
Derivatives
Detect
LPIPs
Estimate
CRF
CRF
Notes: The idea is based on the observation that image gradient contains information about the camera response function. Geometry invariants are independent on the geometry of the locally planar regions in image irradiance. These planar regions in image irradiance is detected using the constraint equation.

## Slide 6: CRF Estimation: Radiometric Calibration
Image © Lin et al.
 Method is edge-based and chooses the best fitting one of the previously learned CRFs from DoRF

## Slide 7: CRF Estimation
What have I done so far?
  Radiometric Calibration almost done
Next steps
  Completing the code on "Radiometric Calibration"
  Start implementing the "Geometry Invariants" paper
  Evaluation
sample patches detected by the algorithm (Radiometric Calibration)

## Slide 8: Evaluation Methods
Synthetically generated Images
  Take direct output of camera sensor (supposed to be linear)
  Manually apply a particular CRF and check if this CRF is found afterwards
Ground Truth Evaluation
  Use a camera with a well known CRF (extract from DoRF)
  Check how far our computed CRFs are from the ground truth
Stability Test
  Obtain series of images taken by the same camera (with fixed camera settings)
  Analyze how much the individual results vary

## Slide 9: Determining the Camera Response Function
Thank you
for your attention!